## Slide 1: ＴｒｉＤｅｆ ３Ｄ変換と２Ｄ互換 Ｅｎｃｏｄｉｎｇ
Julien Flack, Director of Research
3D Consortium, content subcommittee
30th Oct 2003

## Slide 2: ＤＤＤ社
立体映像で１０年の実績を持つ
Autostereoscopic（眼鏡不要）３Ｄ表示装置に注力
Autostereoscopicは科学の視覚表現や広告などに広く使用可
ソフトウェアと２Ｄ／３Ｄ変換サービスを提供
Notes: Dynamic Digital Depth Inc. has been involved in stereoscopic image for over a decade. This experience has culminated in a focus on glasses-free 3D display devices which are finding early adopters in applications such as public space advertising and scientific visualization. DDD provides software and content conversion services to support the emerging stereoscopic 3D displays industry.

## Slide 3: ２Ｄから３Ｄへの変換
２Ｄ－３Ｄ変換はリアルタイムかオフラインで使用
リアルタイム変換技術は２Ｄ映像から指示を受け ビデオレートで３Ｄシグナルへ変換する
オフライン変換技術は人による操作で３Ｄ インフォメーションをビデオへ変換する
この２つの方法は長所と短所があり、それぞれ適したマーケットがある
Notes: 3D Display devices require 3D content. Conversion techniques may be broadly categorised as real-time or off-line.
Real-time conversion techniques integrate the conversion of 2D content within the playback device. The playback device therefore takes a standard 2D video signal as input and produces a 3D signal through image and motion analysis of the 2D image sequence.
Off-line conversion techniques generally rely on user-assisted techniques to recover 3D information from 2D images. The recovered 3D information is encoded and transmitted to the playback device
We will briefly consider the relative benefits and drawbacks of each approach in general terms.

## Slide 4: リアルタイム変換
長所
コンテンツ変換コストが最低限に抑えられる
即時の変換
２Ｄと互換
著作権問題がない
短所
画質の均一性に欠ける
静止画としては普通は不満の残る画質
時に３Ｄは左右の視覚映像を取り違えることがある
多視点表示のサポートが困難
画質のコントロールが困難
Notes: The advantages of real-time conversion is that it is instant and requires no human intervention. The approach is inherently 2D compatible as the conversion can be simply turned off.
The main disadvantage of real-time conversion is that the quality is inconsistent. In general terms, real-time conversion algorithms make assumptions regarding the content. As long as these assumptions hold the quality is good. When the assumptions are not satisfied poor quality stereoscopic images result. Many of these approaches assume simple camera motion which increases the chance of pseudo-stereoscopic 3D. These motion based techniques also cannot convert still images. Finally, it is difficult to quality control real-time converters as playback and conversion are integrated.

## Slide 5: オフライン変換
長所
均一性のある高品質の３Ｄ
２Ｄと互換
全てのタイプをサポートできる（単視点／多視点）
ユーザーが３Ｄ効果の度合いをコントロールできる
画質のコントロールができる。
短所
リアルタイムに比べて変換コストが高い
変換時間；即時にできない
コンテンツのサイズが大きくなる
Notes: Off-line conversion generally involves some form of user interaction in order to reconstruct the 3D geometry of the scene. As such, there are no implicit assumptions about the content. This leads to consistent high quality stereoscopic 3D and as long as the 3D data is carefully encoded 2D compatibility is ensured.
Off-line conversion essentially de-couples conversion and playback making it easier to support a range of different 3D output devices. In addition, consistent user controls for configuring the 3D strength and effects are more easily supported. As the content is converted before playback it is easier to quality control.
The disadvantages of off-line conversion are higher costs and longer timeframes for conversion. As the 3D information is embedded in the media file more bandwidth is required to transmit the data.

## Slide 6: DepthMapを使用しての画像合成
２Ｄ映像
Depth Map
３Ｄ映像
２Ｄ映像とDepth Mapからビデオレートで複数の角度からのビューを生成
[ click for animation]
Notes: DDD’s proprietary conversion and rendering system is based on depth maps. Depth maps are used in conjunction with a 2D image to synthesize perspective views. The views are generated at video rates depending on the 3D display and the observer’s 3D strength and effect parameters settings.

## Slide 7: ２Ｄ映像とDepth Encoding
３Ｄ Depthエンコードフォーマットは２Ｄと互換
一つの（デバイスに依存しない）メディアファイルで広範囲の３Ｄ表示装置に対応
ユーザーはリアルタイムで３Ｄのパラメーターを調整可能
Depth Mapは高圧縮をかけて２Ｄメディアフォーマットに乗せることが可能
単視点＋深度、複数視点＋深度からもっと広い視野角にまでスケーラブルであることがコンセプト
Notes: Encoding stereoscopic content using depth maps has a number of advantages. The format is 2D compatible as the original video signal is transmitted unaltered. As the views are rendered in real-time a single “device agnostic” media file can support a wide range of display devices. Similarly, stereoscopic parameters can be adjusted to fine tune 3D strength and position settings.
As we will describe later, depth maps can be effectively compressed and embedded in existing 2D transmission standards.
The source+depth concept is scalable to stereo+depth and multiview+depth to support wider viewing angles and better handle occlusion effects

## Slide 8: 高速２Ｄ／３Ｄ変換
オフラインで半自動２Ｄ－３Ｄ変換技術を利用してDepth Mapを生成
Depthの情報を増やすために 先進の機械学習アルゴリズムを使用
Depth Mapの再現は９０％正確であることが数値的に示されている
１分のビデオ変換作業は約１０人・時間
ＮＴＳＣの３Ｄ変換サービスは１分間２５００米ドルで提供。
Notes: For the conversion of still images and video sequences DDD employs a semi-automatic approach. In this approach a special effects artists guides an advanced machine learning algorithm to create depth maps. This process is very efficient, typically the user only has to specify depth for approximately 2% of the pixels in the image to create an accurate depth maps. Quantitative tests have shown that we can reconstruct depth maps with 90% accuracy relative to the ground truth.
Commercially we offer this service at a cost of $2,500 USD per minute for NTSC resolution video. It takes our post-production studio approximately 10 person hours/min to convert 2D video to 3D.

## Slide 9: Depth Mapping – TriDef Transformer
ユーザーが指定した
DepthPoint
変換ツール
算出されたＤｅｐｔｈＭａｐ
Notes: The TriDef Transformer takes a single 2D image frame and provides the user with intuitive tools for assigning depth to objects in the image. The conversion paradigm is based on the concept of “scribbling” depth into the image. This interface is simple, easy-to-learn and does not require any specialist 3D knowledge making it easy to quickly train new staff for large conversion tasks.

## Slide 10: Depth “Tweening”
Frame 1- 99
Key Frame 0
Depth map
Key Frame 100
Depth map
Train
Train
Neural Net
Neural Net
Depth
Tween
Classify
Classify
Notes: For the conversion of video sequences key frames are selected and depth mapped. The frames in between key frames are automatically calculated using Depth Tweening. In the depth tweening process machine learning algorithms are used to establish the relationship between the source image and the depth map at key frames. A neural network is an effective machine learning algorithm which is able to establish relationships between the source image and an associated depth map. In this example, it is apparent that there is a high correlation between the colour of the sky and its depth in the key frame (black). The neural network learns a functional relationship of the colour, position and depth of related pixels.
A trained neural network is then used to estimate depth values for all pixels in between key frames.

## Slide 11: Depth Tweening Video
Neural Networkでは元の２Ｄ画像をうまくトラッキングして境界線が正確なDepth Mapを生成することができる
[ Click image for video ]
Notes: This video illustrates that the depth maps generated are edge accurate and consistent over time.

## Slide 12: Stereoから生成したDepth
両眼の視差がDepthMapを補正する。
Left eye
Right eye
Calculated Depth map
Stereo
Analysis
Stereo
capture
[ Click image for video ]
Notes: Depth maps can be automatically recovered from stereo pairs. Stereo a

## Slide 13: 自動深度補正
動きに基づいた構成の技術は、連続する単眼映像から深度を計算するため使用することができるものである
Source Image
Automatically calculated
depth map
[ Click image for video ]

## Slide 14: Depth Mapの圧縮
Depth Mapは３Ｄ画像の質の低減を感じさせることがなく高圧縮をかけることができる
  空間解像度は ４：１に圧縮可能
  最高の圧縮ではDepth Mapを２Ｄ画像２％のサイズまで小さくすることができる
  ２Ｄの互換は維持されている

## Slide 15: スタンダードＭＰＥＧ－２ ｄａｔａ ｓｔｒｅａｍ
DepthMapを組み込んだMPEG-2 Streamは完全にMPEG-2 Streamに準拠しており、２Ｄとも互換 （つまりＤＶＤ互換）
Video
Audio
Depth Mapを組み込んだStream
MPEG-2 compliant data stream
Private

## Slide 16: 先進のDepth圧縮
Neural Network（NN）は２Ｄ画像／Depthの相互関連をエンコードする
NNはわずか20 Bytes/frame
Depth Mapはリアルタイムで再生成される
Depth Mapは（元の）２Ｄ映画像と関連するようにエンコードされている
X
R
G
B
Y
X
Y
Source Image
Depth Map
Neural Net

## Slide 17: まとめとして
ＤＤＤは２Ｄから３Ｄへの変換と２Ｄ互換エンコーディングの特許を下記の国で収得しています（日本、アメリカ、ヨーロッパ、オーストラリア、シンガポール、韓国、カナダ、メキシコ、中国、インドネシア、インド、香港）
弊社のオフラインビデオと静止画映像変換技術は、広範囲の３Ｄ表示装置上で高品質の立体３Ｄを生成します
弊社の２Ｄ互換エンコーディング技術はｂａｎｄｗｉｄｔｈにおいて非常に効率的です